## Slide 1: Outline
Introduction
The ITU-T H.323 Recommendations
Capabilities of present H.323 products

## Slide 2: The ITU-T H.323 Recommendations
H.323 entities
Capabilities of H.323 terminals
  audio, video, data exchanging and processing
  controls issues and device control
H.323 Multipoint Conferences
Capabilities of the H.323 MCU
Control issues

## Slide 3: H.323 Entities
H.323 terminal
H.323 Multipoint Control Unit end-points
H.323/H.32* Gateway
H.323 Gatekeeper

## Slide 4: Defined audio capabilities of H.323 terminals
H.323 terminal
Audio
codec(s)
Audio
channel(s)
G.711 A-law, μ-law
G.722, G.723,
G.728, G.729,
MPEG-1 audio
Coding schemes
Green for mandatory features
Orange for optional features
H.323 terminal
Audio
mixing
multicast
multicast
G.729
G.728
Assymetric operation

## Slide 5: Defined visual capabilities of H.323 terminals
H.323 terminal
Video
codec(s)
Video
channel(s)
H.261 QCIF
H.261 CIF,
H.263 SQCIF,QCIF,
CIF, 4CIF, 16CIF
Coding schemes
Green for mandatory features
Orange for optional features
H.323 terminal
Video
mixing
or
switching
multicast
multicast
QCIF
CIF
Assymetric operation

## Slide 6: Defined data capabilities of H.323 terminals
H.323 terminal
T.120 entity
Data
channel(s)
T.120
Green for mandatory features
Orange for optional features
H.323 terminal
- One or more data channel(s)
- Unidirectional or bi-directional channel(s)

## Slide 7: Audio-visual capabilities of H.323 terminals

## Slide 8: Capability set (CS) of an H.323 terminal
H.245 procedure to exchange CS
Decoder capability set
  video & audio bit rate,
  video, audio format,
  algorithm options accepted by decoder
Number of simultaneous audio, video decoding
Encoder: is free to transmit anything in the agreed set.

## Slide 9: H.323 Multipoint Conferences
Multipoint Controller (MC)
  control functions (e.g., chair control)
  controls MP
Multipoint Processor (MP)
  video
    switching,
    mixing,
    transcoding
  Audio
    mixing,
    transcoding
  T.120 data distribution

## Slide 10: Types of multipoint conferences
Centralized
Decentralized
Hybrid

## Slide 11: Centralized multipoint conferences
unicast
MCU
MP
MCU
H.323 terminal
MCU
MP
MP
MP
MP
MC
MC
MC
Audio & Video
unicasting
Audio & Video
unicasting
Audio & Video
multicasting

## Slide 12: Decentralized multipoint conferences
Audio & Video Multicasting
MP
MP
MP
MP
MC
GW
H.323 terminal
MCU
MC
MC
- 1 MP @ every H.323 terminal
- 1 MC/session @ any H.323 end-point
IP

## Slide 13: Hybrid multipoint, centralized audio
Video Multicasting
MP
MP
MP
MP
H.323 terminal
MCU
- 1 MP for video @ every terminal
- 1 MC/session @ MCU
IP
Audio
unicasting
MC

## Slide 14: Hybrid multipoint, centralized video
Audio Multicasting
MP
MP
MP
MP
H.323 terminal
MCU
- 1 MP for audio @ every terminal
- 1 MC/session @ MCU
IP
Video
unicasting
MC

## Slide 15: Characteristics and potential location of MC and MP

## Slide 16: Defined capabilities of the H.323 MCU
Must Support centralized Mult. conferences
MP
  video switching,
  synchronization and video mixing
  synchronization and audio mixing,
  transcoding,
  T.120 data distribution
MC
  control functions
MC
MCU
MP

## Slide 17: MP functions
sw
MP@MCU
Sa
Sa
Sa
Sa
Video/audio switching function
Sb
Sb
Sd
Sc

## Slide 18: MP functions
mix
Audio/video mixing function
Sa
Sb
Sd
Sc
Mixed(Sa,Sb,Sc,Sd)
MP@MCU

## Slide 19: MP functions
Audio/video transcoding function
trans
MP@MCU
Sa
Sa
Sa
Sa @ QCIF
Sb
Sb
CIF
QCIF
CIF
CIF

## Slide 20: MP functions
sw
MP@MCU
Da
Da
Da
Da
Data distribution function

## Slide 21: Control issues performed by MC (H.243)
Α. Automatic video selection mode
Β. Chair-control mode
  video broadcast visualization forcing capability
  multipoint visualization
  video selection
Any terminal can have the chair token
Floor control - only in chair-control mode
Camera control

## Slide 22: Automatic video switching mode
sw
MP@MCU
Sa
Sa
Sa
Sa
Sb
Sb
Sd
Sc
The selection mechanism is voice-activated

## Slide 23: CC - Video broadcast (VCB)
To determine which one of the available video streams will be transmitted to all terminals, except chairman’s
Sa
Sb
Sd
Sc
MCU
VCB Sb
Sb
Sb
MC
MP
Chair-control
terminal

## Slide 24: CC - Video select (VCS)
To determine which video stream will be transmitted to chairman’s terminal
Sa
Sb
Sd
Sc
MCU
VCS Sc
Sc
MC
MP

## Slide 25: CC - Multipoint visualization (MCV)
To broadcast chairman’s terminal video to all participants
Sa
Sb
Sd
Sc
MCU
MCV
Sa
Sa
Sa
MC
MP

## Slide 26: Floor Control issues performed by MC
Floor control is possible only in chair-control mode.
Any terminal may request the floor by sending command TIF to the MCU.
The MCU forwards the request to the chair-control terminal.
MCU
TIF
MC
TIF

## Slide 27: Camera control (H.281)
A moderator is able to control the local and remote cameras that are connected to an H.323 terminal that supports H.281 standard (FECC: Far-End Camera Control)

## Slide 28: Capabilities of present H.323 terminals

## Slide 29: Required H.323 entities
IP
H.323 & T.120
Multipoint
Conference Unit (MCU)
H.323
Terminal
H.323/H.320
Gateway
ISDN
H.323
Gatekeeper
H.323
Terminal
H.323
Terminal
H.320
Terminal
H.323
Terminal
Wz
Wy
Wx
Wi