## Slide 1: Βασικές αρχές PET, Ραδιοφάρμακα, PET κάμερες
Dr med Γεώργιος Ν. Μπενέτος, MD, MSc, PhD
Ακαδημαϊκός Υπότροφος Α’ Πανεπιστημιακή Καρδιολογική Κλινική
Cardiac CT Κλινική Λευκός Σταυρός
EACVI and SCCT Level 3 certified in Cardiac CT

## Slide 2
Nuclearmedicine vs. Radiology
Transmission
Emission

## Slide 3: PET-CT cameras
Siemens PET-CT camera
GE PET-CT camera

## Slide 4: Digital vs analog PET cameras
Digital (Vereos) vs analog (GEMINI) PET camera
With Digital camera shorter scan times, less FDG (radiation dose), less noisy images
Hatami et al, J Nucl Med Technol 2020

## Slide 5: CT-AC for PET is mandatory
AC
NAC
AC
NAC

## Slide 6
Hybrid-PET/MR
PET
MRI
PET
Metabolism imaging
Coronary flow reserve
Cardiac MRI
Anatomic and morphological information
Functional information
PET/MR
Notes: What if we could combine both methods in a one-stop shop examination in one hybrid machine?

## Slide 7
MRI
PET
Conditions:
MR compatible PET detectors
MR attenuation correction
Hybrid-PET/MR

## Slide 8: What is a positron?
A positron is an anti-matter electron, it is identical in mass but has a positive charge of +1
Positron can come from different number of sources but for PET they are produced by nuclear decay
Nuclear decay is basically when unstable nuclea are produced in a cyclotron by bombarding the target material with protons and as a result a neutron is released
E.g 18-0 enriched water +proton = 18-F + neutron

## Slide 9: How are tracers produced?

## Slide 10: Basic principles
In PET the product of the bombardment decays to a more stable state isotope by emitting a positron, for instance 18-F has too many protons, so one of these protons decays to a neutron emitting in the process a positron and a neutrino
Positron begins its activity by colliding with other particles and gradually losing its kinetic energy

## Slide 11: Annihilation reaction
Notes: ΑΝΤΙΔΡΑΣΗ ΕΞΟΥΔΕΤΕΡΩΣΗΣ

## Slide 12
Annihilation reaction and photon detection
The positron will encounter an electron and completely annihilate each other resulting in converting all their masses into energy. Because of conservation of mass and momentum each photon has energy of 511 kEV and head in an almost 180 degrees from each other
Notes: The positron will encounter an electron and completely annihilate each other resulting in converting all their masses into energy. Because of conservation of mass and momentum each photon has energy of 511 kEV and head in an almost 180 degrees from each other

## Slide 13: PET tracers used in cardiology
Myocardial perfusion tracers: 15O-water, 13N-ammonia, 82Rubidium and 18F-Flurpiridaz
Myocardial metabolism and viability tracer: 18F-Fluorodeoxyglycose
Microcalcification tracer (vulnerable atherosclerotic plaque): 18F-sodium floride

## Slide 14
Tracer Production Half-life
15O-Water Cyclotron 2 min
13N-Ammonia Cyclotron 10 min
82Rubidium Generator 1 min
18F-Flurpiridaz* Cyclotron 110 min
82Rb
13N-NH3
15O-H2O
18F-Flurpiridaz
* currently in phase III study
PET Myocardperfusions-Tracer
modified from Schindler et al. JACC Cardiovasc Imaging. 2010 Jun;3(6):623-40

## Slide 15: 13N-ammonia

## Slide 16: Rubidium 82 PET MPI

## Slide 17: Oxygen-15 water
Oxygen-15 has a short half-life of 2 minutes that is well-matched to the short biological half-life, resulting in a very low radiation dose of 1-2 mSv
It is freely diffusible across capillary and cell membranes with extraction fraction close to 100%
very robust and versatile for the quantification of MBF under many different disease conditions
The washout rate of H2 15O correlates tightly with MBF23 and is considered the gold-standard for quantification of blood flow in the myocardium and other perfused organs.
It is not metabolically retained in tissues, that is RF = 0
Seminars in Nuclear medicine 2020

## Slide 18: 18-F Flurpiridaz
Notes: FDA APPROVAL 09/2024

## Slide 19
Maddahi et al. Semin Nucl Med. 2014 Sep;44(5):333-43.
PET - Perfusion Tracers

## Slide 20: Uptake rate and net uptake
Retention rate (retention fraction)
Uptake rate (EF=extraction fraction)
Seminars in Nuclear medicine 2020

## Slide 21
Coronary Flow
0
1
2
3
4
5
Rest
Exercise
Dipyridamole
Adenosine
Condition
Coronary Flow
(ml/min/g)
Chan. JACC 1992;116:53-58
N-13 Ammonia
Coronary Flow and Stress Tests

## Slide 22
Radiopharmazie ist ein zertifizierter Pharmabetrieb
Herstellung Positronen-
emittierender Nuklide (18F,11C, 13N…)
Dosierung für Patienten (GCP, GLP, GMP…)
Cyclotron
Hotcells/Module
Nuclide | Halftime | FWHM Diameter
15O | 2.04 min | 1.05 mm
13N | 9.96 min | 0.39 mm
11C | 20.4 min | 0.28 mm
18F | 109.7 min | 0.22 mm
Production of PET Tracer - cyclotron

## Slide 23
Production of PET Tracer - generator

## Slide 24: Types of stress
Exercise stress test (treadmill) (target: at least 85% of maximal HR and continue exercise 1 min after the injection)
Pharmacologic vasodilator stress
  Adenosin
  Regadenoson
  Dipyridamol
Pharmacologic synthetic cathecholamin stress
  Dobutamin
Vasodilat.
b1-stim.

## Slide 25
Acquisition Protocol
CTAC

## Slide 26
Myocardperfusions-PET - Semiquantitative
Superior image quality
Common reconstructions as SPECT
Axial
Horizontal long and
vertical long axis view

## Slide 27
Semiquantitative perfusion imaging
But in comparison with myocardial perfusion SPECT:
- with high spatial resolution (4-7mm).
- with high contrast resolution (target to background ratio)
- with accurate attenuation correction
- with very high diagnostic accuracy
- at a low radiation dose exposure (1-2mSv)
Sampson et al. J Am Coll Cardiol 2007;49:1052–8
Bateman et al. J Nucl Cardiol 2006;13:24–33 Di Carli et al. J Nucl Cardiol 2004;11:719 –32 Stewart et al. Am J Cardiol 1991;67:1303–10
Go et al. J Nucl Med 1990;31:1899–1905

## Slide 28
Acquisition Protocol
CTAC

## Slide 29
Dynamic acquisition

## Slide 30
RV
LV
myocardium
Akquisition von Zeitaktivitätskurven
Quantitative Imaging

## Slide 31
Quantitative Imaging
rest MBF (ml/min/g) stress MBF (ml/min/g)
MFR (stress:rest)
MFR normal > 2.5
MFR pathologic < 2.0

## Slide 32
Myocardperfusions-PET - Quantitative
MFR
Hyperemic Flow
Rest Flow

## Slide 33
Problem of MPI: Evaluation of relative tracer uptake may lead to underestimation of the extent of CAD and even uniform tracer uptake despite
  1) extensive (three-vessel) CAD or in the case of 2) endothelial dysfunction or microvascular disease
Balanced CAD patterns in as much as 5-10% of patients with suspected CAD Kajander et al. Circulation. 2008;118:S_1010-S_1011
Why/when is quantitation useful?

## Slide 34: PET and MFR – Prognostic Value
254 patients with ischemic heart failure undergoing PET MPI and viability testing identified from Zurich PET Registry
MFR independent predictor of events in this patient category
Benz D., …Benetos G…Buechel R. JACC Img 2020
Notes: Objectives: The aim of this study was to investigate the prognostic and clinical value of quantitative positron emission tomographic (PET) metrics in patients with ischemic heart failure.
Background: Although myocardial flow reserve (MFR) is a strong predictor of cardiac risk in patients without heart failure, it is unknown whether quantitative PET metrics improve risk stratification in patients with ischemic heart failure.
Methods: The study included 254 patients referred for stress and rest myocardial perfusion imaging and viability testing using PET. Major adverse cardiac event(s) (MACE) consisted of death, resuscitated sudden cardiac death, heart transplantation, acute coronary syndrome, hospitalization for heart failure, and late revascularization.
Results: MACE occurred in 170 patients (67%) during a median follow-up of 3.3 years. In a multivariate Cox proportional hazards model including multiple quantitative PET metrics, only MFR predicted MACE significantly (p = 0.013). Beyond age, symptom severity, diabetes mellitus, previous myocardial infarction or revascularization, 3-vessel disease, renal insufficiency, ejection fraction, as well as presence and burden of ischemia, scar, and hibernating myocardium, MFR was strongly associated with MACE (adjusted hazard ratio per increase in MFR by 1: 0.63; 95% confidence interval: 0.45 to 0.91). Incorporation of MFR into a risk assessment model incrementally improved the prediction of MACE (likelihood ratio chi-square test [16] = 48.61 vs. chi-square test [15] = 39.20; p = 0.002).
Conclusions: In this retrospective analysis of a single-center cohort, quantitative PET metrics of myocardial blood flow all improved risk stratification in patients with ischemic heart failure. However, in a hypothesis-generating analysis, MFR appears modestly superior to the other metrics as a prognostic index

## Slide 35
Prognostic value of MFR in DM
Patients without CAD and DM and abnormal MFR have the same prognosis with patients with DM and known CAD
Patients with DM and normal MFR have the same prognosis with patients without DM and without CAD
Venkatesh et al. Circulation 2012

## Slide 36
Radiation Dose– PET

## Slide 37
Normal relative stress perfusion images and normal MBFR are associated with a very low risk of cardiac death (<0.5% per year)
Myocardial perfusion alone does not exclude:
  a. 50% left main disease,
  b. extensive CAD,
  c. balanced MBF reduction,
  d. extensive microvascular disease,
  e. non-response to vasodilation
Normal MBFR in addition to normal perfusion establishes physiologic normality of the epicardial arteries and the microvasculature.
Knowledge of the total atherosclerotic burden with CACS
Value of PET

## Slide 38: PET tracer used for metabolism - inflammation
18-F FDG
Produced by cyclotron
Half life of 110 minutes
Compound: deoxyglycose

## Slide 39
Hibernating Myocardium in PET
18F-FDG
13N-NH3
MISMATCH
Normal myocytes under fasting conditions consume fatty acids
Postprandial they consume glycose
The chronic reduction of MBF levels that occur with myocardial hibernation leads to an overdependence on glucose metabolism by the cardiac myocyte
Adaptive metabolic change
Notes: The effective dose for a 10- mCi dose of 18F-FDG administered intravenously is 7 mSv.

## Slide 40
Hibernating Myocardium in PET – glycose protocol

## Slide 41
FDG-PET – Basics (inflammation)
Accumulation FDG ~ glucose uptake
Reflects metabolic activity of cells
High uptake in inflammatory cells … but also in any cells that are metabolically very active (sterile inflammation, infection, cancer, physiologically etc.)
FDG
Glucose
GLUT
FDG
Glucose
Hexokinase
FDG-6-Phosphate
Glucose-6-Phosphate
Krebs cycle
Glucose-6-phosphate isomerase
FDG-6-Phosphate
FDG-6-Phosphate
18F-FDG: half life of 110 min
Photons energy 511 kEV
Notes: Different from glucose, the phosphorylated radiotracer,
18F-FDG-6-phosphate does not proceed into glycogen
synthesis or aerobic glycolysis with only minimal dephosphorylation
and return of radiotracer to blood; it is
thus metabolically trapped in tissue. Consequently, its
uptake is reflective of overall glucose uptake

## Slide 42
FDG-PET - Basics
Suppression of myocardial FDG uptake
18F-FDG
Whole-body PET/CT acquisition
Duration of acquisition approx. 20 minutes
+/- CTA
12 hours fasting
No carb / high fat diet
60 mins
uptake
±Heparin
2.5-5MBq/kg
Notes: 5-15 mCi (185-555 MBq)
10 MCI=7MSV

## Slide 44
Hibernating Myocardium in PET
18F-FDG
13N-NH3
MISMATCH
Normal myocytes under fasting conditions consume fatty acids
Postprandial they consume glycose
The chronic reduction of MBF levels that occur with myocardial hibernation leads to an overdependence on glucose metabolism by the cardiac myocyte
Adaptive metabolic change
Notes: The effective dose for a 10- mCi dose of 18F-FDG administered intravenously is 7 mSv.

## Slide 45
PET-FDG Myocardial Viability - Case
CTO RCA and EF=40%
Source USZ

## Slide 46
Source USZ
Anterior MI and CTO LAD
PET-FDG Myocardial Viability - Case

## Slide 47
USZ:
n = 1341 pts
Median: 1.3mSv
Case et al. J Nucl Cardiol. 2017 Aug;24(4):1427-1439
Radiation Dose– PET

## Slide 48
Advantages
  Availability (SPECT)
  Exercise test (SPECT)
  Claustrophobia (SPECT)
  Renal and liver function not relevant
  No allergic reactions
  Devices do not alter the quality of the examination
  Quantification of myocardial flow (PET)
  Low radiation (PET)
Pros and Cons of SPECT and PET
Disadvantages
  Availability (PET)
  High radiation (SPECT)
  Claustrophobia (PET)
  Balanced ischemia (SPECT)

## Slide 50: Tracer uptake increases proportionally to MBF
Myocardial uptake of 201Tl increases proportionately with perfusion when perfusion increases up to 2–2.5 times above resting levels before reaching a plateau in myocardial uptake.
The 99mTc-labelled tracers reach a plateau in myocardial uptake at a myocardial perfusion around twice resting levels

## Slide 51
rest MBF (ml/min/g) stress MBF (ml/min/g)
MFR (stress:rest)
Myocardperfusions-PET – Flow quantification
MFR normal > 2.5
MFR pathologic < 2.0
Notes: By drawing activity time curves (by placing specific ROIs) we can calculate myocardial blood flow both in stress and rest

## Slide 52
Nuclear Cardiology – Myocardperfusion PET
LOR
Annihilation
g
g
„Single“ event
„Single“ event
Notes: Annihilation of a proton with an electron to two high energy photons (511kEV)

## Slide 53
Dewey M et al. Nat Rev Cardiol. 2020.
PET - Perfusion Tracers

## Slide 54: Prognostic value of MFR in DM
Venkatesh et al. Circulation 2012
Retrospective study of 2783 pts (1172 DM and 1611 without) who underwent RB PET perfusion imaging. Median FU of 1.4 years
Notes: Background—
Diabetes mellitus increases the risk of adverse cardiac outcomes and is considered a coronary artery disease (CAD) equivalent. We examined whether coronary vascular dysfunction, an early manifestation of CAD, accounts for increased risk among diabetics compared with nondiabetics.
Methods and Results—
A total of 2783 consecutive patients (1172 diabetics and 1611 nondiabetics) underwent quantification of coronary flow reserve (CFR; CFR=stress divided by rest myocardial blood flow) by positron emission tomography and were followed up for a median of 1.4 years (quartile 1–3, 0.7–3.2 years). The primary end point was cardiac death. Impaired CFR (below the median) was associated with an adjusted 3.2- and 4.9-fold increase in the rate of cardiac death for diabetics and nondiabetics, respectively (P=0.0004). Addition of CFR to clinical and imaging risk models improved risk discrimination for both diabetics and nondiabetics (c index, 0.77–0.79, P=0.04; 0.82–0.85, P=0.03, respectively). Diabetic patients without known CAD with impaired CFR experienced a rate of cardiac death comparable to that for nondiabetic patients with known CAD (2.8%/y versus 2.0%/y; P=0.33). Conversely, diabetics without known CAD and preserved CFR had very low annualized cardiac mortality, which was similar to patients without known CAD or diabetes mellitus and normal stress perfusion and systolic function (0.3%/y versus 0.5%/y; P=0.65).
Conclusions—
Coronary vasodilator dysfunction is a powerful, independent correlate of cardiac mortality among both diabetics and nondiabetics and provides meaningful incremental risk stratification. Among diabetic patients without CAD, those with impaired CFR have event rates comparable to those of patients with prior CAD, whereas those with preserved CFR have event rates comparable to those of nondiabetics.

## Slide 55
Herzog et al. J Am Coll Cardiol. 2009 Jul 7;54(2):150-6
Prognostic value of CFR

## Slide 56
PACIFIC trial. Danad I et al. JAMA Cardiol. 2017 Oct 1;2(10):1100-1107.
n = 208
Head-to-head diagnostic performance

## Slide 57
Blood compartment
Ca(t)
Tissue Ct(t)
Myocardium Cm(t)
Extravascular
compartment
K1
k2
modified from Schelbert et al. Circ 1981
Metabolic compartment
k3
k4
15O-water
18F-flurpiridaz
13N-ammonia
82Rb
Myocardial compartment model