## Slide 1: Pipelining
Example of a Pipeline with 5 stages:
  Fetch
  Decode and read operands in registers
  Use ALU to execute instruction or to calculate memory address
  Read or Write to memory
  Write result back to Register file
Remark: not all instructions use step 4 and 5
source: wikimedia.org (CC)
Notes: Notation: the green blocks represent registers that store the result of a pipeline stage
1- Fetch: use the PC as the address to access memory and get the code of an instruction. Result: binary instruction code
2- Decode: interpret the binary instruction code to determine the operation to be performed and its operands; access the register file to obtain the instruction operands. Result: values to be sent to ALU, control signals to the datapath
3- Execute: perform a logic/arithmetic operation on the operands; OR calculate the address to access data memory. Result: ALU output (operation result or memory address)
4- Memory Access: if the instruction is a LD (memory read) or ST (memory write), access memory
5- Write Back: if the instruction produces a result to be stored in a register, the result being either the result of the ALU calculation or a value read from memory, write to the register file.

## Slide 2: benefits of Pipelining
For the previous example of a 5 stage pipeline, the execution over time is presented in this diagram.
Note that although each instruction takes 5 clock cycles to execute, due to pipelining, after filling the pipeline, on every clock another instruction finished its execution.
Effectively, the number of instructions executed per second is the same as the clock rate.