## Slide 1: Memory Hierarchy: search for data at the highest level: Hit or Miss and search in the lower level

## Slide 2: Actual Connection

## Slide 3: Rough Approximation for Access Time vs Volume

## Slide 4: L1 cache: for instructions- access no delay L2 cache: for data- access with 1-2 cycles delay

## Slide 6
Segment: a set of data (or code) that belong to the logical entity, e.g. data of a process, code of a program.
Page: a set of contiguous data (words in memory) that are a power of 2, e.g. 128 contiguous words, 512 (29 ) contiguous words , 4096 (212 )contiguous words.
Memory Management (Mem Mgt)
1) Bitmap

## Slide 7: Linked List: each record contains the beginning and ending address of either an unused space or used by a segment. Four examples with unused spaces (holes) and spaces used by segments

## Slide 8: Algorithms for “Where to write a new Segment” (Mem MGT with Segments)
Searching an unused space (hole) to store a new segment
First fit: the first unused space (hole) that can contain the segment.
Best fit: the smallest unused space (hole) that can contain the segment.
Worst fit: the largest hole that can contain the segment.
Buddy’s Algorithm: we keep lists for holes. Each list has the holes with the same “hole size” as powers of 2. Each time that we have a segment S of size |S|, 2k-1 <|S|≤ 2k , we write the S into the first hole in the list of size 2k and the rest of the space we split into powers of 2 and add to the other lists.
  Example: |S|=491, write in a hole of the list 512 (29 ) and create new holes in the lists with sizes 16, 4 and 1.
  Fastest, best space management, needs the logistics overhead (lists).
External Fragmentation: the set of spaces between contiguous segments that are small and cannot be used by the newly created segments.

## Slide 9: Virtual Memory: a mapping function of Virtual Addresses onto Real Addresses.
Implemented by a memory called Look Up Table (LUT)
Use of Pages: to reduce the size of the LUT
Handled by the Memory Management Unit (MMU)

## Slide 11: Memory access
Use Associative Memory (Translation Lookaside Buffer) to speed-up the search.
If we find the page (data) in memory: hit
If we do not find it: miss, we have a page fault and it has to fetch it from the HD
For large memories: multilevel page tables
Internal Fragmentation: the unused space of a file within its pages.

## Slide 12: Multi-level Page Table

## Slide 13: Segments needed to distinguish logic entities: data, code, etc. Segmentation with Paging: Virtual Address Translation

## Slide 14: Content Addressable Memory (CAM)

## Slide 15: Interleaved Memory

## Slide 16: Page Replacement Algorithms
Least Recently Used (LRU): A linked-list of pages. The page that is used takes the “head” of the list. We store back (or overwrite) the “tail” page.

## Slide 17: Working Set (with clock) WSClock
The set of pages that a process is currently using is its working set
make sure that it is in memory before letting the process run
Load the working set before the process runs:
prepaging ( vs paging on demand )
WSClock: circular list of page frames
  pages are added, they go into the list to form a ring.
  Entries of a page record: a) Time of last use b) R –referenced-bit c) M –modified-bit. A pointer (hand of the cclock) shows the last reference page.
  at each page fault the page pointed to by the hand is examined first. If the R bit is set to 1, the page has been used during the current tick. Set R=0 and hand=hand->next.
  If the age is greater than τ and the page is clean, it is not in the working set: overwritten.
  If M=1: schedule the page’s HD transfer and search for another clean page.
  Efficient almost as LRU, easiest, cheapest to implement.

## Slide 22
Example of computing the page size
Needs a lot of parameters, here we consider only:
  average process size: s bytes
  page size be p bytes
  each page entry (LUT) requires e bytes
approximate number of pages per process is then s/ p,
occupying (se / p) bytes of page table space.
last page’s internal fragmentation is p/2
overhead = (se / p) + p/2
First derivative with respect to p and equating it to zero
1/2